## Slide 1: CSE 321 Real Time and Embedded Operating Systems
Project 3, Fall 2022
Joseph Yang

## Slide 2: Table of Contents
Introduction
Project Overview
Internal Features
Development Timeline
Block Diagram
Diagram of System
Bill of Materials
User Instruction
Result
Notes: Add hyperlinks to each slide

## Slide 3: Introduction

## Slide 4: Introduction
This project falls under the category of neurodiversity. It is designed to help people who think differently than others. Some have their own preference of communication with other people such as communicating through morse code.

## Slide 5: What is needed to solve the problem
Design a product that makes individuals more comfortable communicate with other people

## Slide 6: Real World Safety Critical
Design must effectively communicate with others with high accuracy
Doing so would prevent any miscommunications to occur

## Slide 7: Project Overview

## Slide 8: Project Overview
Objective: Translate morse code given from the user and display it on the LCD

## Slide 9: Specifications
LCD must be used
At least two keys on the matrix keypad be used
A external input peripheral: IR sensor
A external output peripheral: Buzzer
Watchdog timer must be configured
Uses of Synchronization technique
At least 1 bitwise driver configuration
Critical Section protected
At least 1 interrupt
A task/thread incorporated

## Slide 10: Features
Left IR sensor gives ‘.’ and right IR sensor gives ‘-’
With every input detected, the buzzer makes noise
With every input detected, the LCD will display user’s input
Keypad ‘1’ translate user input and display the character in the LCD
Keypad ‘2’ clear user input if they make a mistake
Keypad ‘3’ clear user input and translated code

## Slide 11: Application
System can be used for:
Radio communication
Implement passwords for any locks
People who likes to communicate in morse code

## Slide 12: Internal Features

## Slide 13: Watchdog
Watchdog is a way to resets the system in case of any failures or malfunction
Watchdog is implemented to reset the LCD if the system assumes the user is inactive for more than 30 seconds
Global:
Main:

## Slide 14: Watchdog
With every input, the function will reset the watchdog to assume user is still using the system

## Slide 15: Synchronization Technique
A synchronization technique is a way to have multiple threads running simultaneously cooperate to each other.
Mutex is used in this project, it allows multiple thread to take turns in sharing resources

## Slide 16: Synchronization Technique
Mutexes are used on the IR sensors so it can have access to the signal variable one at a time.
It doesn’t confuses what to put in for the user input

## Slide 17: Bitwise Driver
Bitwise driver is controlling the bits in the microcontroller that makes the pins act a specific way
The main program changes specific pins to read an input and provide an output
Below here makes one of the pin to provide voltage

## Slide 18: Protect The Critical Section
Critical section is protected by using an EventQueue that allows synchronization between multiple threads
EventQueue is used for the IR sensors

## Slide 19: Protect The Critical Section
By using EventQueue it’s to ensure that any inputs given from the IRs will be safe and won’t mess up the shared resources. In this case that would be the signal and user_input global variables
Main code:

## Slide 20: Thread/Task Incorporated
A thread/task having a program do another task in parallel with the main program or main thread
The thread is used to print in serial monitor how long the program has been running for using the timer API

## Slide 21: Thread/Task Incorporated
In main:
The function that is called every 5 seconds

## Slide 22: Interrupts
An interrupt is when the system sees a certain event, it halts the main program and do it’s own thing. Once the task is done, it returns back to the main program.
Interrupts is used on PD6, 7, or 8. These pins will trigger when it notices a rising edge.
Global:
Main:

## Slide 23: Interrupts
Functions that will call when an interrupt occurs

## Slide 24: Development Timeline
Start
The day project 3 was assigned
11/7/22
Peripherals
Learned how to use an IR sensor and a buzzer
11/20/22
Program created
A proper code was made to somewhat function correctly
11/25/22
Functionality
The code works perfectly as intended however, not all project requirements have been met
12/6/22
Requirement met
Watchdog timer, Mutexes, thread/task, and critical section protection successfully implemented into the project
12/14/22

## Slide 25: Block Diagram

## Slide 26: Diagram of System
Flowchart ->

## Slide 27: Bill of Materials
Component | Quantity | Purpose | Additional Notes
LCD | 1 | Display text to user | 1602 Model
Nucelo | 1 | Run the program and make connections to other peripherals | L4R5ZI Model
Matrix Keypad | 1 | Controls LCD display | 4x4 Keypad
Breadboard | 1 | Placeholder for peripherals | 
Jumper Wires | 120 | Make Connections | Require some male to female & female to male wires
LED | 1 | Display Input | 
Resistor | 1 | Prevent LED to blow up | 
Buzzer | 1 | Make noise | 
IR | 1 | Take user input | 

## Slide 28: User Instructions

## Slide 29: Schematic
Notes: Show breadboard, LCD, LED, and nucleo connections

## Slide 30: Instruction to Build
1. Connect first row pin of matrix keypad to PD7 using jumper wires.
2. Connect column one pin to PD6, column two pin to PD5, and column three pin to PD4 using jumper wires.
3. Connect 5V from the nucleo to the breadboard's red power rail.
4. Connect the GND from the nucelo to the breadboard's blue power rail.
5. Connect the LCD's SDA to PB9, and SCL to PB8. Finally connect the the GND to the breadboard's blue power rail and Vcc to the red power rail.
6. Place the buzzer on the breadboard. Connect Vcc to PD10, it's I/O to PC11, and it's GND to blue power rail.
7. Place two IR sensors on the breadboard. Connect both IR sensor's GND to blue power rail and Vcc to red power rail.
8. Connect the left IR sensor's OUT to PC8 and the right sensor to PC9.

## Slide 31: Instruction to Use
Left IR gives ‘.’
Right IR gives ‘-’
1 on keypad translates code
2 on keypad clears input
3 on keypad clears input and message

## Slide 32: Test Plan
Things to Test | Inputs | Outcome
IR sensors | Hover finger around left IR twice and the right IR one | LCD displays “..-”
Buzzer | Hover finger around IR sensors as many times as you like | Buzzer should make a noise for every input
Keypad 1 | Give inputs “.---” Press 1 Give inputs “-.--” Press 1 | LCD displays “JY”
Keypad 2 | Give any inputs Press 2 | LCD should show user input, then the user input screen is cleared
Keypad 3 | Give inputs “.-” Press 1 Give inputs “...” Press 3 | LCD should show message as “A” and user input as “...” Once 3 is pressed it clears message and user input

## Slide 33: Result

## Slide 34: Result
All requirements were successfully implemented into the project
IR sensor have taken in user input correctly
Program successfully translated morse code
Results shown properly in the LCD

## Slide 35: Future Considerations
Sometimes the program ignores the IR sensor
1 IR sensor would be more appropriate

## Slide 36: Considerations - General Improvement
Implementation on muxes, and Eventqueue improve the program:
Made IR sensor pickup user input faster
Code ignores user input a lot less but it still happens

## Slide 37: References
https://www.geeksforgeeks.org/map-associative-containers-the-c-standard-template-library-stl/
https://cplusplus.com/reference/map/map/find/